## Slide 1
HVAC Optimization Project
WWW.REALLYGREATSITE.COM
01
TEAM: ​
ANANYA WADHWA​
AVNEET SINGH​
CARLOS NAKAGOMI​
SUNAINA JAIN​

## Slide 2
02
One-Week-Ahead HVAC Forecasting & Optimization
  Objective: Reduce HVAC electricity use based on predicted building occupancy.
  Tools used: Time series (STL), Random Forest, SVR, FNN.
  Focus Week: January 1–7, 2006.
  Outcome: Achieved 14.5% reduction in energy use.

## Slide 3
03
Why This Work Is Important
  This project addresses a critical issue in building energy management. HVAC systems are one of the largest consumers of electricity, and when operated inefficiently — for instance, during off-hours or when rooms are empty — they contribute heavily to waste.
  Our objective is to make HVAC operations more intelligent by predicting occupancy and using that to guide energy use. It’s important because it not only saves money and energy but also supports global sustainability goals and regulatory compliance.
  The solution we’re developing can be applied in smart buildings, universities, offices, and even homes to cut costs and carbon footprints. It’s a scalable solution that balances comfort and conservation — two core priorities in energy-efficient building design.

## Slide 4
04
Methodology overview
  Occupancy Forecasting: The number of occupants was forecasted at 10-minute intervals using time-series and machine learning techniques.
  Feature Engineering: Time-based features, lagged occupancy values, and weather-related parameters were engineered.
  Machine Learning Models: Two models were used: Support Vector Regression (SVR) and Feedforward Neural Network (FNN).
  HVAC Optimization: The predicted occupancy was utilized to design a rule-based control strategy that adjusts HVAC operation based on occupancy and weather.

## Slide 5
05
Dataset & Features –
How We Built the Foundation
Data Source: Synthetic dataset (10-min intervals) for 2005–2006.
Feature Types:
- Time-based: hour, minute, day_of_week, is_working_hour
- Occupancy-based: current & lagged occupancy
(t, t– 30min to t–2h)
- Weather-based: temperature, heating/cooling degree
days, snowfall
We engineered features from three main categories — time, occupancy, and weather. These capture both the predictable structure and dynamic behavior that influence HVAC demand. Lagged occupancy values allow the model to anticipate future needs, which is essential for pre-conditioning indoor spaces.

## Slide 6
06
STEP 1:
PREDICTION OF NUMBER OF OCCUPANTS
Method Used: STL Decomposition (Seasonal-Trend Decomposition using Loess)
  Extracted seasonal daily cycles (144 intervals/day)
  Averaged trend over time
  Removed residual noise
Two seasonal baselines used:
  Jan–Mar 2005 (Spring)
  Oct–Dec 2005 (Fall)
Result: Stable weekday patterns with clear working-hour peaks and low off-hour occupancy.
Objective: Forecast the number of building occupants for the week of Jan 1–7, 2006.

## Slide 7
07
STEP 2: HVAC SCHEDULE FORECAST
After creating features like lagged occupancy, time indicators (hour, day, is_weekend), and weather data, we merged everything into a final dataset called final_df. This dataframe contained all inputs needed to predict HVAC energy usage.
Following are some important columns we engineered for this step:
• occupants_t, occupants_t_minus_30min, …, occupants_t_minus_2h: Occupancy
history
• hour, minute, day_of_week, is_weekend, is_working_hour: Time context
• mean_temp, heat_deg_days, total_precip: Weather conditions
• hvac_energy_kWh: Simulated energy based on rule (target column)

## Slide 8
08
Simulating HVAC Energy
  If no occupants → 0.0 kWh (HVAC off)
  If working hour (8 AM TO 6 PM) → 0.25 × occupants
  Otherwise → 0.15 × occupants
  Gives a baseline consumption estimate
This logic reflects how HVAC systems behave in real life. The idea is to use more energy when the building is occupied and scale it down when it's empty. This provided us with a benchmark to later compare the performance of ML models.

## Slide 9
09
HVAC ENERGY
PREDICTION MODELS
We built two models:
1. SVR (Support Vector Regressor)
2. FNN (Feedforward Neural Network)
These models learn from the patterns in occupancy, time, and weather to predict how much HVAC energy will be used.
Real-world impact of this step:
By training ML models to predict HVAC energy usage, facility managers can:
• Forecast demand and plan for energy loads.
• Use predictions to simulate and test HVAC schedules.
• Integrate these forecasts into automation systems to dynamically adjust HVAC settings.

## Slide 10
10
RESULTS
OF MODELS
SVR Model Performance:
  MAE: 0.1233
  MSE: 0.0335
  RMSE: 0.1830
  R²: 0.9996
Even though SVR has a slightly lower MAE, the FNN is still a top performer — especially as it can learn more from data over time.
Thus, FNN was selected for scheduling.
FNN Model Performance:
  MAE: 0.1910
  MSE: 0.0785
  RMSE: 0.2802
  R²: 0.9992

## Slide 11
11
Optimizing HVAC Scheduling
STEP 3:
Turn HVAC ON 2 hours before occupancy and OFF 2 hours after.
Applied on full dataset using fnn_predicted_hvac_kWh.
• Result:
• Baseline usage: 8635.90 kWh
• Optimized usage: 8629.09 kWh
• 🔋 Saved: 6.81 kWh (0.08%)
Strategy 1: FNN + Smart Rule (Pre-Cool & Post-Cool Window)
Strategy 2: Smart Rule-Based Logic
If occupancy = 0 AND it’s non-working hours → HVAC OFF
Result:
• Baseline usage: 8636.33 kWh
• Optimized usage: 9149.81 kWh
• Increased usage by 5.95%
📉 So this strategy was less effective.

## Slide 12
To conclude, I successfully replicated a research paper that uses machine learning and occupancy-based scheduling to optimize HVAC energy consumption. I broke this down into three phases: occupancy prediction, HVAC energy forecasting, and schedule optimization.”
“I trained ML models like SVR and FNN, simulated smart control strategies, and tested two different logic systems for turning the HVAC on and off.”
“The strategy that combined machine learning with rule-based scheduling saved energy while still maintaining comfort — which is exactly what modern smart buildings aim for.”
12
CONCLUSION

## Slide 13
In the real world, this kind of system can be deployed in offices, universities, malls, and even airports — anywhere HVAC consumes a large share of electricity. Over time, even a small improvement like 0.08% energy savings per week can result in thousands of dollars saved per year, and help contribute to sustainability goals like carbon reduction and net-zero buildings.”
“More importantly, it shows how data, ML, and smart logic can work together to build more intelligent and energy-efficient environments.”
13
REAL WORLD USAGE

## Slide 14
14
thank
you!